## Slide 1: Automated Transport Vehicle
Michael Esposito
B.S., Computer Science
Email: michael5486@gwu.edu
Cell: (908) 418-1063
Notes: Introduction
Hi everyone, for those that don’t remember me I am michael, and today I will be introducing you to the automated transport vehicle, or ATV for short

## Slide 2: You Need to carry things, but are incapable
Applies to those that are:
  Physically handicapped
  Temporarily handicapped
  Lazy people
What if there was a robot that could carry your heavy items?
Notes: If I asked you to name one issue that occurs frequently in your daily life, what would you say? I’m sure a good amount of us needed the ability to carry a large amount of things, but for some unfortunate reason were incapable of doing so. Having the ability to carry extra cargo would be helpful for many groups of individuals, mainly those that are
physically handicapped…they could be blind, weak joints, missing a limb and restricteed to crutches for example.
past couple months I wasunable to carry heavy loads because of shoulder injury...a robot that could help carry heavy loads would have been higly beneficial for myself and others with temporary handicaps. This brings us to the big question...what if there were a robot that could carry heavy loads?

## Slide 3: What Can the Automated transport vehicle Do?
Carry items up to 20 lbs
Navigate through various environments
Follow a user at speeds up to 5 mph
Avoid obstacles
Notes: I present to you my proposal for an automated transport vehicle that can solve such problems.
able to carry something the size of a carry-on suitcase, and weighs anywhere under 20 pounds.
able to navigate through various environments…cover rural, outdoorsy areas, urban settings with curbs, people, and slight inclines like our GWU environment, and anything in between.
ATV can follow behind a user that is moving at a speed up to five miles an hour, and will categorize and algorithmically determine a near-optimal path to avoid obstacles and continue to track its user. The vehicle will have water-resitant properties to promote all-weather functionalities, and will be constructed in a way that promotes being both lightweight and safe.

## Slide 4: How does it work?
Onboard cameras – detect and locate user, objects
Sensors – detect, classify, and identify objects
Single-board computer – processes image feed, algorithmically tracks users and identifies near-optimal route to avoid objects
Rocker-Bogie – suspension arrangement that provide all-terrain traversal and cargo stabilization
Cargo area opening assist
Notes: This system sounds pretty cool, right? But how will it work?
Camera will take in a visual feed, pass it through to onboard computer that hosts our visual processing system. Here, it will look for its target and continuously send signals to the motors if its course needs to be adjusted
A series of onboard sensors will map the robot’s surrounding, and help locate and decide the robot can climb over an object or requrie a new path and reidentification of the target user
A single-board computer will be used to analyze the image feed from the cameras, combine that with sensor data, and determine a route for the robot. Single board computers are like the Raspberry Pi that we all hear about…they house all the components required for a computer on...you guessed it...a single board. This serves to reduce our power consumption and overall weight of the robot so we can prolong battery life.
This rocker bogie is a complicated-soundinng concept at first, and I will explain more of it in a little bit, but most importantly it is a mechinsm that serves to suspend this robot in a way that can traverse many types of terrain. It holds the cargo area between two sets of wheels in the air, and will keep it secure and relatively flat so components and cargo remains flat and safe.
And lastly, the cargo compartment itself will be roomy, and keep its contents safe from the elements. It will have an auto-opening assist much like the type you see on the trunks of newer cars...as in the compartment door will open and close with the push of a button. This is to help a potentially disabled user’s tasks easier, and reduce the strain required to load the device.

## Slide 5: User Recognition
Front-facing RGB camera can identify user, isolate them from background
Compare images to previously-gathered image data, identify bodily features, obtain center-of-mass and coordinates for user
Notes: User recognition will be a difficult task for this project, but the underlying algorithms can be briefly explained. The front facing RGB camera, taking in a constant source of pictures, needs to isolate a target user from background garbage. Camera needs to operate in various conditions and lighting situations, but some assumptions can make the job easier. A
Assume that for the vast majority of the time, the robot will be tracking the back side of the user, and doesn’t really care about finer features like hair color or clothing color or anything of that sort. It needs to look for it common traits among humans, like a head, shoulders, and arms like in this diagram on the left. We can compare image data to previously gathered data…and if any image features and blobs look like these pictures on the right, for example, the target’s location can be calculated.
Once a coordinate for the target is acquired, the robot can modify its course as required. Now so far we have talked about robot movement minus the presence of any obstacles, so that brings us to the next section… (press aroww)

## Slide 6: Object Recognition
Mounted distance sensors can detect and create mapping of objects near the user and ATV
On-board computer records and interprets sensor data, decides if object is traversable or avoidable
  Decides upon a near-optimal path to avoid objects and continue following user
Notes: With our product, the user does not need to worry when stepping over a curb, on dirt, or goes around a corner quickly. This is meant to be a press-and-forget device. To accomplish this, the ATV utilized multiple sensors mounted across the front of the device to detect obstacles. As you can see, in the diagram on the left, a series of distance sensors can begin to create a computerized representation of the real world. As objects are detected, the robot will be forced to either go over or around obstacles, and can make multiple movements to do so. Decisions will be chained together, and as this middle diagram illustrates, encountered objects will create this tree-like structure of points that this robot will be able to navigate through in order to stay close behind its target.

## Slide 7: Vehicle Construction
Rocker-bogie Mechanism – used on Mars rovers, provides ability to climb inclines, curbs and other objects less than 6 inches in height
Cargo compartment automatically opens and closes, and it stabilized so cargo will remain flat and secured
Selected material will be lightweight, but sturdy enough to hold cargo and survive daily wear-and-tear
Notes: Skipping this to shorten time, but know that selected materials will be lightweight, sturdy yet inexpensive to provide the most
bang-for-the-buck once this product hits the market
Lastly, I’ll cover the robot construction choices. As stated before, the Rocker-bogie sounds complicated, can be worked successfully with these Lego pieces over here. It is a six-wheeled design, and as the Mars rovers can demonstrate, provides ample ability to climb objects smaller than 6 inches. The cargo compartment will remain stabilized, so cargo is kept secure. And our selected materials will be lightweight, sturdy, yet inexpensive, in order to achieve our design metrics and provide the most bang-for-the-buck once this devices hits the market.

## Slide 8: How Is it better than the competition?
Combines inexpensive materials and simplified designs to accomplish our goal
Other devices navigate using a predefined map to get from point A to point B
Automated cars satisfy a different purpose, do not offer off-road traversal and cargo assistance
Strong construction, simplified design and ease-of-use make this product a viable option for disabled individuals to reduce bodily strain
Notes: One more thing you may be thinking is, great, this is cool and everything, but how is it better than some competitors already out there? We’ll I’ll tell you!
ATV combines inexpensive materials and simplified designs to accomplish our goal. It is actively scouting out it’s environment, and not reliant on a predefined set of locations to get from point a to point b.
Our robot provides some capabilities provided by an automated car, but an automated car accomplishes a completely different design objective than what we are offering. Our device is something you can take in the house, out of the apartment, throw some books in on the way to class or work and then pick some things up at the store. IT is meant to be a tool, an extension of your ability.
And as such, it’s strong construction, simplified design and ease of use will make it a viable option for disabled individuals looking for a way to reduce bodily strain.

## Slide 9: For more Information
Email: michael5486@gwu.edu
Project Outlines, Requirements and Specifications and other documents: https://gw-cs-sd.github.io/sd-2017-human-tracking/